## Slide 1
Helmut Habersack, Marlene Haimann, Philipp Gmeiner, Sandor Baranya, Katarína Holubová, Florin Vartolomei
DanubeSediment
Danube Sediment Management – Restoration of the Sediment Balance in the Danube River
• SEDIMENT ALTERATION – A SIGNIFICANT WATER MANAGEMENT ISSUE IN THE DANUBE RIVER BASIN

## Slide 2: Main objectives of DanubeSediment
To propose a transnational sediment monitoring network
To establish for the first time the sediment budget for the Danube River considering the input of the most important tributaries as well,
To identify reaches with surplus and deficit, river bed aggradation and degradation, sediment-related problems in flood risk management, hydropower generation, navigation, ecology
To gain knowledge and better understanding of sediment transport and morphodynamic processes
To develop a Danube Sediment Management Guidance (DSMG) and a related Sediment Manual for Stakeholders (SMS)

## Slide 3: Sediment deficit
 Reduction of sediment input to Black Sea by about 60 %
(DanubeSediments, 2019)

## Slide 4: Sediment (Dis)balance
Sediment budget:
(based on Frings et al., 2014b)
(DanubeSediments, 2019)
Historic situation
Existing situation

## Slide 5
Stanica & Panin, 2009
Tescari et al., 2006
Kuroki et al., 2006
Coastal Erosion
Coastal erosion up to 24 m / year
Coastal erosion

## Slide 6
Channel length change
Danube in Germany
reference state
present state
Upper Danube: -38 %, Middle Danube: - 6 %, Lower Danube: -5 %
Channel width change
Upper Danube: -39 %, Middle Danube: - 12 %, Lower Danube: - 0,4 %
Length and width change

## Slide 7
Sediment alteration –
river bed change
Goda et al., 2007
modified after Batuca et al., 2002
Erosion: 55 % (29 %)
Sedimentation: 36 %
Equilibrium: 9 %
Morphological Change

## Slide 8
Remobilisation in a reservoir during 2002 and 2013 floods
Question of sediment release
Release: 5,5 Mio. m3
Source: viadonau, Verbund
Sedimentation in impoundments

## Slide 9:  ICPDR 3rd Danube River Basin Management Plan
Alteration of sediment balance
Based on key findings of the DanubeSediment project the alteration of the sediment balance is now identified as new sub-item of the Significant Water Management Issue “Hydromorphological alterations”. The aim is to fully integrate this issue into the development of the 3rd DRBMP Update 2021.
Significant Water Management Issue

## Slide 10: Significant Water Management Issue (SWMI) report
Vision
The ICPDR’s basin-wide vision is a balanced sediment regime and an undisturbed sediment continuity. Type-specific natural bed forms and bed material as well as a dynamic equilibrium between sedimentation and erosion is provided. The balanced sediment regime enables the long term provision of appropriate habitats for the type-specific aquatic communities and water dependent terrestrial ecosystems.
Significant Water Management Issue

## Slide 11
Location of selected measures within the basin
Catchment scale
land use - optimized cultivation
land use - afforestation
improved sediment continuum
1
2
3
1
2
3
Reach / sectional scale
reservoir – flushing, bypass, turbidity current
free flowing section – widening, side channel reconnection
4
5
4
5
5
Local / point scale
at the dam – weir height, sediment turbine, elevation of outlet and intake structures
free flowing section – feeding
6
7
7
6
Danube Sediment Management Guidance (DSMG)

## Slide 12
  General Recommendations
  Development of a basin-wide sediment management concept
  Improvement of legal regulations and governance
  Preservation of the sediment continuity and the morphology
  Restoration / Improvement of the sediment continuity
  Reduction of surplus and deficit reaches
  Development and implementation of sediment related measures addressing navigation, hydropower and flood risk management
  Defined refeeding of the dredged material
  Adapted land use, reduced sediment outputs from agriculture
  Establishment of harmonized sed. monitoring network and data management
  Sediment quality needs to be included
  Sediment related risk analysis
  Stakeholder involvement and interdisciplinary planning
  Adaptive implementation of measures and accompanying monitoring
Danube Sediment Management Guidance (DSMG)

## Slide 13
The Danube River features a totally disturbed system (sediment continuum interruption, sediment disbalance).
Sediments are essential for hydromorphology, thus for ecology, but also an essential aspect for hydropower, navigation, flood risk management etc.
Cumulative effects on sediments arise not only from upstream to downstream but also backwards.
It has to be considered that sediment processes differ between each river section
(Upper Middle Lower Danube Danube Delta).
The alteration of sediment balance becomes a Significant Water Management Issue in the DRBMP.
Conclusions

## Slide 14: Many thanks for your attention!
Univ. Prof. DI Dr. Helmut Habersack
Chair on Hydraulic Engineering and River Research
UNESCO Chair on Integrated River Research and Management
Christian Doppler Laboratory for Sediment Research and Management
Institute of Hydraulic Engineering and River Research
Department of Water, Atmosphere and Environment
BOKU – University of Natural Resources and Life Sciences, Vienna
Muthgasse 107, 1190 Wien
Tel.: +43 1 47654 0
Fax: +43 1 47654 149
helmut.habersack@boku.ac.at
http://www.wau.boku.ac.at

## Slide 15: Part C: Good practice examples for sediment management measures
Different categories of measures:
1) State of the art
2) Tested (implemented at least once)
3) State of science
Subdivided in 4 chapters:
DanubeSediment
Sediment Manual for Stakeholder (SMS)

## Slide 16: Sediment management measures
against erosion in free flowing sections
(modified after Habersack et al., 2013)
against sedimentation in reservoirs
DanubeSediment

## Slide 17: Part C: Good practice examples for sediment management measures
Good practice examples:
- Measures for improving the continuity of sediment transport
- described in a standardized way incl. figures, tables, photos and a summary of practical experiences, qualitative cost estimation
Recommendations for Stakeholders
DanubeSediment
Sediment Manual for Stakeholder (SMS)

## Slide 18
Sediments – Floods – Hydropower
Habersack et al., 2017
Bedload and suspended sediment measurement

## Slide 19
DanubeSediment
source: Verbund/viadonau
Reservoir sedimentation and remobilisation

## Slide 20
Sediments: Deposition in floodplains
(Gmde Ardagger Markt, Pressl, 2013)
Machland
Sedimentation during flood 2013
Verbund, Schmallfuss, 2013)
Eferdinger Becken
Habersack et al., 2015