## Slide 1: Assessment of Statistical Significance of Historic Danube Floods
Dr. Stevan Prohaska, Aleksandra Ilić, Dr. Pavla Pekarova

## Slide 2: Theoretical basis for the statistical significance of historical floods assessing
Theoretical flood hydrographs of different probabilities of occurrence whose parameters are: maximum ordinate (peak) and maximum flood wave volume.
Qmax,p – maximum hydrograph ordinate;
Wmax,p – maximum hydrograph volume;
TB,p - total time of flood hydrograph (hydrograph base time).
Danube Conference 2019

## Slide 3: For theoretical floods of probability of occurence: p(Qmax ) = p(Wmax)= p(%) →R(Qmax:Wmax)=1.0
In practice 0 < R < 1.0
Theoretical basis for the statistical significance of historical floods assessing
Danube Conference 2019

## Slide 4: Serbian experience
In practice 0 < R < 1.0
At 132 hydrological stations of the the Republic Hydrometeorological Service of Serbia (RHMSS)→
from R(Q;W) = 0,013 (h.s Bistrica, r. Bistrica)
to R(Q;W) = 0,895 (h.s Ćemanov most, r. Tamnava).
 | R(Qmax : Wmax) |  |  |  |  |  |  |  | 
Range | 0.000-0.100 | 0.101-0200 | 0.201-0.300 | 0.301-0.400 | 0.401-0.500 | 0.501-0.600 | 0.601-0.700 | 0.701-0.800 | 0.801-0.900
Frequency (h. s.) | 1 | 9 | 10 | 19 | 20 | 33 | 22 | 15 | 5
Danube Conference 2019

## Slide 5: In case when R(Qmax : Wmax) < 1.0 we have to define the joint-probability function of the two hydrograph parameters: - peak discharge (Qmax) and - maximum volume of floods (Wmax)
Serbian experience
Danube Conference 2019

## Slide 6: Bivariate probability of occurrence of flood parameters
PROIL model:
Density functions – the lines of same bivariate probabilities of occurrence:
F(Qmax;Wmax) = p, for p = 0.1, 1.0, 2.0 and 5.0%, and
Bivariate exceedance probabilities function:
P {(Qmax≥ qmax,P)∩(Wmax ≥wmax,P) } = P, for P = 0.1, 1.0, 2.0 and 5.0 %.
Danube Conference 2019

## Slide 7
MODEL PROIL
Bivariate probability if x=Qmax and y= Wmax
Density function
Bivariate exceedance probability function:
Danube Conference 2019

## Slide 8
In the final version of the Chapter 10 of project No9 FRDRB these GS are included:
GS Ingolstadt,
GS Regebsburg,
GS Hofkirchen,
GS Achleiten,
GS Bezdan,
GS Bogojevo,
GS Smederevo,
GS Orsova.
As examples in this presentation the results only for two gauging profiles at the Danube will be presented: Achleiten and Bezdan
Danube Conference 2019

## Slide 9: Bivariate probability of occurrence of flood parameters
Correlation between the considered flood hydrograph parameters of the Danube River were:
GS Achleiten
Coefficient of linear correlation R = 0. 472;
Standard error of correlation coefficient σR = 0.077,
and GS Bezdan
Coefficient of linear correlation R = 0. 405;
Standard error of correlation coefficient σR = 0.091.
Danube Conference 2019

## Slide 10: Bivariate probability of occurrence of flood parameters
The Danube R.
H. S. Achleiten
The Danube R.
H. S. Bezdan
Danube Conference 2019

## Slide 11: Return periods of historic floods along the Danube from GS Berg to GS Orsova
 | Gauging profile | Number of flood waves at GP | P{(Qmax≥ qmax,P)∩(Wmax≥wmax, P)} = P<p=1% |  | T (years) | Analyzed period
 |  |  | Historic flood |  |  | 
 |  |  | Year | p |  | 
1 | Berg | 1 | 1988 | 0.33 | 300 | 1930-2007
2 | Ingolstadt | 1 | 1965 | 0.20 | 500 | 1924-2013
 |  | 2 | 1999 | 0.20 | 500 | 
3 | Regensburg | 1 | 1988 | 0.25 | 400 | 1924-2013
 |  | 2 | 2013 | 1.00 | 100 | 
 | Hofkirchen | 1 | 2013 | 0.65 | 150 | 1901-2013
5 | Achleiten | 1 | 2013 | 0.10 | 1000 | 1901-2013
 |  | 2 | 1965 | 0.20 | 500 | 
 |  | 3 | 1954 | 0.20 | 500 | 
6 | Vienna | 1 | 1965 | 0.20 | 500 | 1828-2006
 |  | 2 | 1975 | 0.25 | 400 | 
 |  | 3 | 1954 | 0.33 | 300 | 
7 | Bratislava | 1 | 1965 | 0.20 | 500 | 1876-2015
 |  | 2 | 1899 | 0.33 | 300 | 
 |  | 3 | 2013 | 0.40 | 250 | 
 |  | 4 | 1876 | 0.90 | 110 | 
8 | Bezdan | 1 | 1965 | 0.25 | 750 | 1931-2016
9 | Bogojevo | 1 | 1965 | 0.80 | 125 | 1931-2016
10 | Pančevo | 1 | 2006 | 1.00 | 100 | 1931-2016
11 | Orsova | 1 | 2006 | 1.00 | 100 | 1840-2016

## Slide 12: PHOTOS OF REGISTERED FLOODS IN THE DANUBE RIVER
Floods markers in Melk
Floods markers in Emmersdorf

## Slide 13: PHOTOS OF REGISTERED FLOODS IN THE DANUBE RIVER
Observed an reconstructed historical floods in Bratislava

## Slide 14
Thank you!